## Slide 1
METHODOLOGY · CAPSTONE 2
Physics-Informed Variational Autoencoding
for Three-Compartment Prostate MRI
Parameter Estimation
Sabyasachi Chowdhury, Aaron Garay
Research Capstone · Homework 2 · Advisor review
Methods only — no
experimental results
are reported in this deck.
Notes: Framing: this is the methodology section, not a results talk. Everything here is either implemented in the repo or explicitly flagged as planned. I'll assume familiarity with PIA and the PIVA architecture and focus on what is specific to this study: the three-compartment prostate model, the two-tier design, and the full-covariance ILR posterior.

## Slide 2
Research Question
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
1
To what extent can physics-informed autoencoding models recover compartment-specific diffusivity, transverse relaxation, and tissue volume fractions from noisy three-compartment prostate MRI signals more accurately than nonlinear least squares — and can a full-covariance variational posterior provide useful and calibrated uncertainty at a clinically representative noise level?
Why a controlled synthetic experiment is the right instrument
Ground truth is known
Every synthetic voxel has a true θ ∈ ℝ⁹, so estimates can be compared directly against truth rather than a proxy.
Noise is a free variable
Rician σ can be varied while the underlying biology is held fixed, isolating noise robustness from model error.
Coverage is measurable
Posterior interval coverage can be assessed directly — impossible on clinical MRI without a per-parameter reference standard.
Scope note: synthetic validation establishes computational feasibility. No claim of clinical validity is made at this stage.
Notes: The question has two halves and they get judged differently. Half one is a point-accuracy claim against NLLS. Half two is a calibration claim, and it is deliberately scoped to sigma = 0.05, the clinical reference level. The synthetic design is not a convenience — it is the only setting where coverage of a latent microstructural parameter can actually be checked.

## Slide 3
Study Design: Two Linked Experimental Tiers
Both tiers share one acquisition grid, one cohort generator, and one held-out test set.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
2
TIER 1
Broad robustness comparison
Five estimators × four noise levels
Estimators
NLLS · PIA · 3 diagonal-PIVA variants
Noise
σ ∈ {0.01, 0.03, 0.05, 0.08}
Varies
Physiological constraint width: tight / doubled / unconstrained positive
Asks
Does accuracy degrade gracefully with noise?
TIER 2
Focused posterior-structure comparison
Diagonal vs. full-covariance at the clinical level
Estimators
Diagonal Gaussian PIVA vs. Full-covariance Cholesky PIVA with ILR fractions
Noise
σ = 0.05 only (clinical reference)
Varies
Posterior covariance structure and volume-fraction latent representation
Asks
Does posterior structure buy calibrated uncertainty?
Held fixed within a tier: acquisition grid · clean test parameters · noisy test observations · physiological ranges · evaluation functions. Tier 2 additionally matches encoder widths, optimizer, epochs, σ_obs, KL warm-up, free-bits, and MC sample count across the two models.
Notes: Tier 1 is the wide sweep: it tells us whether physics-informed amortized inversion beats NLLS at all, and how each family behaves as noise grows. Tier 2 is the actual contribution — it holds everything constant except posterior covariance and the fraction parameterization, so any difference is attributable to those two choices. Worth flagging to the advisor: Tier 2 is a matched-pair design, which is what makes the paired bootstrap valid.

## Slide 4
Variables and Operationalization
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
3
INDEPENDENT
– Estimator family: NLLS · PIA · PIVA
– Noise level: Rician σ on unit-scale S₀
– Constraint width: tight / doubled / unconstrained
– Posterior covariance: diagonal or full Gaussian
– Fraction latent: three-logit softmax or 2-D ILR
DEPENDENT
Primary — estimation error for D, T₂, and v
Secondary
– Coefficient of determination R²
– Pearson agreement r
– Posterior coverage
– Calibrated interval width
– Reconstruction loss
– Computational behavior
CONTROLLED
– Acquisition grid ℰ × ℱ
– Clean test parameters
– Noisy test observations
– Physiological ranges
– Evaluation functions
Tier 2 only
– Encoder widths, optimizer, epochs
– σ_obs, KL warm-up, free-bits
– Monte Carlo sample count
Design consequence: factors 4 and 5 are varied together in Tier 2 — the full-covariance model is also the ILR model. The comparison therefore identifies the joint effect of the two changes, not each one separately.
Notes: Be honest about the confound on this slide before the advisor finds it: in Tier 2, covariance structure and the ILR reparameterization move together. We are measuring the combined effect. Isolating them would need a third arm — diagonal + ILR — and that is a reasonable thing to ask for. Have an answer ready: it is cheap to add, one more 200-epoch run.

## Slide 5
01
Forward Model, Cohort, and Data
What the signal equation encodes and how synthetic patients are built
Notes: Transition: from design to the actual generative machinery.

## Slide 6
Forward Model and Acquisition Grid
A fixed, differentiable signal equation — it is also the decoder in PIA and PIVA.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
4
S(b, TE; θ) = S₀ ∑c∈𝒞 vc exp( − bDc / 1000 ) exp( − TE / T2,c )
S₀ = 1000 (stored signal scale) · b in s/mm² · D_c in 10⁻³ mm²/s, divided by 1000 to reconcile units · TE and T₂,c in ms
Acquisition grid — 16 channels per voxel
ℰ = {0, 150, 1000, 1500} s/mm²
ℱ = {0, 13, 93, 143} ms
Cartesian product: 4 diffusion weightings × 4 echo times = 16 measurements.
Observed input per voxel: xᵢ ∈ ℝ¹⁶
Target vector — 9 tissue parameters
θᵢ = [ Dep, Dst, Dlu, T2,ep, T2,st, T2,lu, vep, vst, vlu ]ᵀ ∈ ℝ⁹
Compartments c ∈ 𝒞 = {epithelium, stroma, lumen}
Simplex constraint: vc ≥ 0, ∑ vc = 1
Physiological ranges encoded in the cohort generator
Compartment | Dᴄ range (10⁻³ mm²/s) | T₂,ᴄ range (ms)
Epithelium | 0.30 – 0.70 | 20 – 70
Stroma | 0.70 – 1.70 | 40 – 100
Lumen | 2.70 – 3.00 | 500 – 1000
Why these three compartments. This is the VERDICT-style tissue model of Panagiotaki et al. (2014). Lumen is separated from epithelium and stroma by roughly an order of magnitude in both D and T₂ — which is what makes the 16-channel grid informative in the first place.
Notes: Two things to stress. First, this equation appears twice — it generates the data and it is the decoder. That is the inverse crime, and it is on the limitations slide. Second, the grid is small: 16 measurements to constrain 9 parameters. That is why the problem is ill-posed enough to be interesting and why a population prior does real work.

## Slide 7
Synthetic Patient Cohort: Hierarchical Generator
Variation is injected at two levels so between-patient phenotype is separable from within-patient heterogeneity.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
5
Volume fractions
Patient phenotype mp ∼ Dirichlet(1.6, 1.8, 1.6)
Concentration αp = 1 + 18 mp
Voxel fractions vpi ∼ Dirichlet(αp)
Each patient gets a characteristic mean composition while voxels retain within-patient heterogeneity.
Diffusivity and relaxation
Patient centers = population mean + Gaussian offset
δpD ~ N(0, diag(0.025², 0.060², 0.020²))
δpT2 ~ N(0, diag(4², 6², 55²))
Voxels sampled around each patient's centers
σvoxelD = (0.04, 0.12, 0.03) σvoxelT2 = (6, 8, 70) ms
All centers and voxel values are clipped to the physiological ranges.
Training and held-out cohorts
40,960
Clean pairs
80 patients × 512 voxels
61,440
After bootstrap
120 patient IDs sampled with replacement
122,880
Training set
× 2 independent Rician noise realizations
240
Held-out test
24 patients × 10 voxels separate seed
All estimator families are evaluated on the same 240-voxel held-out cohort. Tier 1 creates separate fixed-noise observations at each σ; Tier 2 uses σ = 0.05.
Notes: The hierarchy matters for a reason the advisor will care about: voxels within a patient are correlated, so the effective biological sample size is 80, not 120 and certainly not 122,880. The bootstrap multiplies records, not biology. That shows up again in the limitations — the Tier 2 bootstrap resamples voxels rather than patients, which likely understates uncertainty.

## Slide 8
Rician Noise Model and Computational Pipeline
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
6
Rician noise augmentation
x = √( (s + εr)² + εi² ), εr, εi ∼ 𝒩(0, σ²)
– Signals divided by S₀ before noise, multiplied back after
– Training: σ ∼ Uniform(0.01, 0.08) drawn per voxel
– Evaluation: fixed σ for controlled SNR comparison
Why Rician rather than Gaussian
Magnitude MRI is formed from real and imaginary Gaussian components, so the magnitude distribution is not Gaussian at low signal levels (Gudbjartsson & Patz, 1995). The high-b, long-TE corner of the acquisition grid is exactly where signal is smallest — precisely where a Gaussian noise assumption would misstate the likelihood and bias the fit.
Pipeline — generation to evaluation
1 PRIORS
Physiological
ranges per
compartment
2 GENERATOR
Patient-level then
voxel-level
sampling
3 FORWARD MODEL
Eq. (1) on the
4 × 4 grid
→ s ∈ ℝ¹⁶
4 RICIAN NOISE
σ ∈ {0.01, 0.03,
0.05, 0.08} at
evaluation
5 DATASETS
122,880 train
240 held-out
test voxels
6 ESTIMATION
NLLS · PIA · diagonal PIVA · full-covariance ILR PIVA
7 POSTERIOR SAMPLING
25 MC samples (Tier 1) · 300 MC samples (Tier 2)
8 EVALUATION
MAE, R², r · coverage · paired bootstrap · conformal
Notes: Note the asymmetry in the noise protocol: sigma is randomized during training so the encoder learns to be noise-aware across the whole range, but fixed at evaluation so comparisons happen at controlled SNR. That is deliberate — it means one trained model is evaluated at all four noise levels rather than four separately trained models.

## Slide 9
02
Estimators
One baseline, one deterministic inverse map, two variational posteriors
Notes: Transition. Keep PIA and diagonal PIVA brief — advisor knows them. Spend the time on the full-covariance ILR model.

## Slide 10
Estimators at a Glance
All four consume the same 16-channel input and are scored on the same held-out cohort.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
7
 | NLLS (baseline) | PIA (deterministic) | Diagonal PIVA | Full-cov. ILR PIVA
Output | Point estimate | Point estimate | Diagonal Gaussian posterior | Full Gaussian posterior
Inference | Per-voxel optimization | Amortized | Amortized | Amortized
Latent | 8 free params, v_lu = 1 − v_ep − v_st | 9 outputs, softmax fractions | z ∈ ℝ⁹ | z ∈ ℝ⁸, ILR
Decoder | Eq. (1) | Eq. (1), no trainable layers | Eq. (1), fixed | Eq. (1), fixed
Objective | Bounded least squares, Eq. (2) | MSE(ŝ, s) over 16 channels | MSE(ŝ, s) + β D_KL β = 0.1 | Gaussian NLL + β D_KL σ_obs = 0.05
Optimizer | SciPy trust-region reflective, 5000 evals | Adam, 1e-4, 200 epochs | Adam, 5e-4, wd 1e-5, 200 epochs | Adam, 5e-4, wd 1e-5, 200 epochs
Tier | 1 | 1 | 1 (3 variants) | 2
Shared encoder across all three neural models: 16 → 64 → 128 → 256 → 512 → 512, Leaky-ReLU, separate heads for D, T₂, and v. Diffusivity and relaxation outputs are mapped into physiological intervals by mean-plus-scaled-tanh. Gradient-norm clipping at 1.0 throughout. Ground-truth parameter MAE is monitored during training but never enters the optimized loss.
Notes: The key column is the right one. Everything else is context. Two design points worth defending: the decoder has zero trainable parameters in all three neural models — the physics is fixed, not learned — and ground-truth MAE is monitored but never optimized, so the models never see theta during training. They are trained purely on signal reconstruction.

## Slide 11
The Focused Contribution: Full-Covariance ILR Posterior
Adapted from the physics-structured VAE of Finkelstein et al. (2026), applied to the three-compartment prostate setting.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
8
Full covariance via Cholesky factor
qϕ(z | x) = 𝒩(μ, LLᵀ)
z = μ + Lε, ε ∼ 𝒩(0, I₈)
– L ∈ ℝ⁸ˣ⁸ lower-triangular, positive diagonal
– 8 latent coordinates: 3 diffusivities + 3 relaxation times + 2 composition coordinates
– Can represent correlation among tissue parameters — a diagonal posterior structurally cannot
DKL = ½ [ tr(LLᵀ) + μᵀμ − d − 2 ∑ log Ljj ] (4)
ILR coordinates for volume fractions
c = Ψ zv, v = softmax(c)
– Ψ ∈ ℝ³ˣ² is an orthonormal ILR basis
– Its columns lie in the sum-zero subspace
– A two-dimensional z_v parameterizes the three-part simplex, dropping the redundant direction of three-logit softmax (Aitchison, 1986)
Why it matters for a covariance. Three logits for a 3-simplex have one unidentified direction. A full covariance over that redundancy is not meaningful; ILR removes it first.
Tier 2 objective and training protocol — identical for both models
ℒfocused = ℒNLL + β DKL where ℒNLL = (1/16) ∑ ½ [ (xm − x̂m)² / σobs² + log(2πσobs²) ]
Likelihood against the noisy observation, not MSE against the clean signal · KL warm-up linear 0 → 1 over the first 20% of epochs · Free-bits floor λ_fb = 0.5, explicitly monitored because clamping can zero the gradient below the floor
Notes: This is the slide to slow down on. Three arguments to make. One: a diagonal posterior cannot express the D-T2-v correlations that the forward model obviously induces — compartments trade off against each other. Two: ILR is not cosmetic. Putting a full covariance on three softmax logits means modeling a direction that has no effect on v, so ILR is a precondition for the covariance to be interpretable. Three: Tier 2 switches from MSE-to-clean to NLL-against-noisy, which is the statistically correct objective when you intend to make calibration claims. Expect a question on the free-bits floor — answer: it is monitored, and we report whether it binds.

## Slide 12
03
Analysis and Evaluation
Pre-specified metrics, inference procedure, and decision criteria
Notes: Transition to how the study will be judged — criteria fixed in advance.

## Slide 13
Analytical Methods
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
9
Point-estimation accuracy
– MAE — primary measure, stays in the natural units of each parameter
– R² — explained variation against a constant baseline; negative values indicate performance worse than predicting the mean
– Pearson r — linear agreement only
Reported separately for D, T₂, and v. Correlation alone is never treated as evidence of accurate absolute recovery.
Raw posterior coverage
Ĉ0.95 = (1/N) ∑ 1{ θitrue ∈ Ii0.95 } (5)
– 95% percentile interval built from the 300 Monte Carlo samples
– Computed separately for each of the 9 compartment parameters
– Posterior sampling: 25 samples per test input (Tier 1) · 300 samples (Tier 2)
Paired bootstrap comparison
Δb = ĈFullILR,b − ĈDiagonal,b (6)
– B = 1000 paired draws
– The same voxel-index sample is used for both models in each draw — pairing removes comparison noise (Efron & Tibshirani, 1993)
– 2.5th and 97.5th percentiles of {Δ_b} form the 95% percentile interval
Split-conformal calibration
ai = |yi − μ̂i| / max(σ̂i, 10⁻⁸) → [ μ̂i ± q̂ σ̂i ] (7)
– Held-out cohort split into equal calibration and evaluation halves
– q̂ = finite-sample corrected (1 − α) quantile, α = 0.05
– Tests whether the learned uncertainty scale can be corrected post hoc to nominal marginal coverage (Angelopoulos & Bates, 2021)
Notes: The logic chain here is deliberate. Raw coverage asks whether the posterior is calibrated as-is. The paired bootstrap asks whether any difference between the two models is real or sampling noise. Conformal asks a different question — if the raw scale is wrong, can a single scalar fix it, and at what cost in interval width. A model can fail raw coverage and still be useful if conformal repairs it cheaply.

## Slide 14
Pre-Specified Evaluation Criteria
Fixed before external clinical evaluation — stated in advance to constrain interpretation.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
10
1
Primary point accuracy
At σ = 0.05, a physics-informed model beats NLLS for a parameter family when its held-out MAE is lower. MAE is primary because it stays in natural units.
2
Noise robustness
Performance inspected across all four σ. A useful model degrades gradually rather than failing abruptly at the clinical reference level.
3
Agreement
R² and Pearson r are interpreted alongside MAE. High correlation alone is not evidence of accurate absolute recovery.
4
Raw uncertainty
A nominal 95% interval counts as adequately calibrated when |Ĉ₀.₉₅ − 0.95| ≤ 0.05 on held-out data.
5
Posterior structure
Evidence that FullILR changes raw coverage requires the paired bootstrap 95% interval for Δ to exclude zero. Coverage bought only with excessively wide intervals is not an improvement.
6
Conformal sharpness
Among models reaching approximately 95% conformal coverage, smaller mean interval width indicates greater sharpness.
7
Reconstruction
Reconstruction loss is a training diagnostic only — low reconstruction error is insufficient because multiple parameter combinations generate similar signals.
Reporting: evaluation tables report D, T₂, and v separately. For Tier 2, coverage and interval widths are additionally reported for all nine compartment-specific parameters.
Notes: The point of pre-specifying is that criterion 5 has teeth. If the bootstrap interval for delta includes zero, we do not get to claim the full-covariance posterior helped — regardless of the point estimate. And the width clause stops us from declaring victory by simply inflating intervals. Criterion 7 guards the identifiability problem: the decoder can reconstruct well from wrong parameters.

## Slide 15
Limitations and Threats to Validity
Stated up front — several of these bound what the synthetic tier can support.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
11
DESIGN VALIDITY
Synthetic-data validity
The same forward equation generates the data and decodes predictions — an inverse crime. Clinical MRI adds misspecification, motion, and unmodeled compartments. Establishes feasibility, not validity.
Population-prior dependence
Estimators learn from fixed ranges and one hierarchical generator. Apparent performance may partly reflect shrinkage toward the synthetic population.
No spatial or diagnostic endpoint
Voxels are estimated independently. No test of cancer classification, biopsy avoidance, or patient outcomes.
STATISTICAL POWER
Effective sample size
Bootstrapping multiplies records, not biology. Effective biological n remains bounded by the 80 base patients.
Patient clustering
Voxels within a patient share phenotype. Point metrics flatten voxel-compartment values and the Tier 2 bootstrap resamples voxels, not patients — this may understate uncertainty. A patient-cluster bootstrap is preferable.
Small focused test cohort
240 voxels from 24 patients, split into two ≈120-voxel halves for conformal calibration. Compartment-level coverage estimates can be variable.
IMPLEMENTATION & INFERENCE
NLLS simplex constraint
v_ep + v_st ≤ 1 is not imposed during optimization, so a negative derived lumen fraction is possible.
Model-selection bias
Variants and β values examined on a common reference cohort with no distinct validation split.
Single seed, fixed hyperparameters
Differences may be sensitive to initialization, optimizer noise, width, and free-bits.
Uncertainty interpretation
MC variability misses model-form error and population or acquisition shift. Conformal gives marginal, not conditional, coverage.
Notes: Lead with the inverse crime — it is the biggest one and the advisor will raise it if I don't. The honest framing: this tier is a feasibility and calibration study, and the external cohort is where validity gets tested. The two I would most like guidance on are the patient-cluster bootstrap (should Tier 2 be rerun resampling patients?) and model-selection bias (is a three-way patient split worth the loss of training data at n = 80?).

## Slide 16
Not Yet Implemented — Planned Work
Explicitly marked in the methodology; none of these are represented in the current repository.
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
12
Spearman rank agreement
ANALYSIS
ρ_s = corr(R(y), R(ŷ)) with average ranks for ties. A model may preserve voxel ordering despite nonlinear scale compression. Secondary metric — will not replace MAE.
Multi-seed model stability
ANALYSIS
Retrain each final architecture with ≥ 5 independent PyTorch seeds on the same patient-level cohorts. Summarize MAE, R², coverage, and width by mean, SD, and a seed-level CI — separating architecture effects from optimizer randomness.
External clinical validation
DATA
De-identified multi-b, multi-TE prostate MRI from an independent cohort. Inclusion requires the modeled acquisition values or a documented harmonization procedure. Patient-level separation preserved between development and evaluation.
Planned clinical evaluation
ENDPOINT
Protocol compared against ℰ and ℱ before inference. Parameter maps reviewed for physiological plausibility, failure rates, and scanner/site sensitivity. Where histopathology exists, associations analyzed at patient or lesion level — never treating voxels as independent.
Governance: the implemented work is entirely synthetic — no PHI, no human-subject recruitment, no access approval. Any clinical extension requires de-identification, secure storage, access controls, a data-use agreement, and institutional review. Clinical data will be split by patient, never by voxel.
Notes: Frame this as sequencing, not as gaps. Multi-seed is the one that gates the Tier 2 claim — a single-seed architectural difference is not publishable, and it is five runs. That is the cheapest high-value next step and I'd propose doing it before anything else.

## Slide 17
Questions for Discussion
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
13
Should Tier 2 be re-run with a patient-cluster bootstrap?
The current bootstrap resamples voxels, treating correlated within-patient voxels as independent. This likely narrows the interval for Δ and makes criterion 5 easier to pass than it should be. Re-running at the patient level is cheap and more defensible.
Do we need a diagonal + ILR arm to break the confound?
Tier 2 varies covariance structure and fraction parameterization together, so it identifies their joint effect. One additional 200-epoch run would separate them — is that worth it, or is the joint contrast the claim we actually want?
Is multi-seed the right next milestone before external data?
Five seeds per architecture would convert the Tier 2 comparison from suggestive to inferential. Alternative: prioritize securing the external cohort first and accept single-seed synthetic results as preliminary.
How should model-selection bias be handled at n = 80 patients?
A three-way patient split costs training data we may not have to spare. Nested patient-level resampling is the alternative but is considerably more expensive.
Notes: These are the four places where advisor input actually changes what I do next. Lead with the bootstrap question — it is the one that most affects whether the Tier 2 result stands up. Have a recommendation ready for each rather than presenting them as open-ended.

## Slide 18
References
Physics-Informed Variational Autoencoding — Three-Compartment Prostate MRI
14
Aitchison, J. (1986). The Statistical Analysis of Compositional Data. Chapman and Hall.
Angelopoulos, A. N., & Bates, S. (2021). A Gentle Introduction to Conformal Prediction and Distribution-Free Uncertainty Quantification. arXiv:2107.07511.
Efron, B., & Tibshirani, R. J. (1993). An Introduction to the Bootstrap. Chapman and Hall/CRC.
Finkelstein, A., Moneta, R., Zohar, O., Rivlin, M., Zaiss, M., Friedmann Morvinski, D., & Perlman, O. (2026). Multiparameter Uncertainty Mapping in Quantitative Molecular MRI using a Physics-Structured Variational Autoencoder. arXiv:2602.03317.
Gudbjartsson, H., & Patz, S. (1995). The Rician Distribution of Noisy MRI Data. Magnetic Resonance in Medicine, 34(6), 910–914.
Higgins, I., Matthey, L., Pal, A., Burgess, C., Glorot, X., Botvinick, M., Mohamed, S., & Lerchner, A. (2017). beta-VAE: Learning Basic Visual Concepts with a Constrained Variational Framework. ICLR.
Kingma, D. P., & Welling, M. (2014). Auto-Encoding Variational Bayes. ICLR. arXiv:1312.6114.
Panagiotaki, E., Walker-Samuel, S., Siow, B., Johnson, S. P., Rajkumar, V., Pedley, R. B., Lythgoe, M. F., & Alexander, D. C. (2014). Noninvasive Quantification of Solid Tumor Microstructure Using VERDICT MRI. Cancer Research, 74(7), 1902–1912.
Raissi, M., Perdikaris, P., & Karniadakis, G. E. (2019). Physics-Informed Neural Networks: A Deep Learning Framework for Solving Forward and Inverse Problems Involving Nonlinear Partial Differential Equations. Journal of Computational Physics, 378, 686–707.
Thoreau, R., Risser, L., Achard, V., Berthelot, B., & Briottet, X. (2025). Physics-Informed Variational Autoencoders for Improved Robustness to Environmental Factors of Variation. arXiv:2210.10418v5.
Virtanen, P., et al. (2020). SciPy 1.0: Fundamental Algorithms for Scientific Computing in Python. Nature Methods, 17, 261–272.
Reproducibility: notebooks contain the acquisition grid, seeds, physiological ranges, cohort sizes, model definitions, optimizer settings, and evaluation code. Dependencies are pinned in requirements.txt. Reproduction runs top-to-bottom from a clean environment without reusing hidden notebook state.
Notes: Two anchors worth naming aloud if asked: Thoreau et al. for the PIVA formulation itself, and Finkelstein et al. for the full-covariance posterior direction — their PS-VAE does this for quantitative molecular MRI, and this project ports the idea to the three-compartment prostate setting.